## Slide 1: Internet of Things (IoT) Professor: Dr. Sadoon Azizi s.azizi@uok.ac.ir Faculty of Engineering Department of computer and IT engineering

## Slide 2: Chapter objectives
* Students must learn these subjects in this chapter:
TCP/TP reference model in traditional inernet
Application layer
Transport layer
Network layer (Internet layer)
Datalink layer

## Slide 3
Application: supporting user applications
  FTP, SMTP, HTTP
Transport: Process of data transmission
  TCP, UDP
Network: Routing datagrams (packets) from source to destination
  Routing protocols, IP
Datalink: Data transportation between midpoints (Host, router, switch, etc.)
  Ethernet, 802.11 (WiFi), PPP
Physical: Bit transportation on the physical medium
Internet protocol stack

## Slide 4
Email
Web
News groups
Remote access
P2P file transfer (such as Bittorretn)
Online multiplayer games
Video sharing (such as Youtube)
Voice over IP (such as Skype)
Social networks (such as Facebook)
Search
…
Some network applications

## Slide 5: Network application creation
Network Applications:
Run on different edge devices
Connect over network
  For instance web service provider contacts the browser
There is no need to program the core devices
Core does not run user applications
This architecture facilitates speed and difficulty of network applications’ development
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 6: Network applications’ architecture
There are two major architectures for network applications:
Client-Server (Customer-Provider)
Peer to Peer (P2P)

## Slide 7: Client-Server architecture
Service provider:
Host always up and running
Static IP address
Using datacenters in case of huge scale processings
Client:
Initiates connection with provier
Can have dynamic IP address
Do not connect directly
Client/Server

## Slide 8: P2P architecture
Service provider isn’t always on
Edge devices connect to each other directly (service request and reply)
  Self-scale: Users are increasing the service capacity on one hand and on the other they increase the service request.
Cost friendly architecture
It’s does not coordinate with the ISP policies, security and intensions.
Peer to Peer

## Slide 9: Web and HTTP
A review on HTTP
A webpage consists of different things.
  Such as HTML file, JPEG picture, Java applet, audio file, etc.
The most important part of a web page is an HTML file which references other things.
References are made with a URL, such as:
www.someschool.edu/someDept/pic.gif
Hostname
Object path

## Slide 10: A review on HTTP
HyperText Transfer Protocol (HTTP)
Application layer protocol for web
Client-Server model
  Client: A browser that requests, receives and shows web contents.
  Server: Web service provider which replies the needed content to the requests that users made.
PC running
Firefox browser
server
running
Apache Web
server
iphone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 11: Transport services and protocols
Creates a logical connection between the running application processes on different hosts
Transport protocols run on the edge systems
  Sender: breaks the sending messages into segments and delivers them to the network layer
  Receiver: Gathers the segments and delivers them to the application layer
Two transport protocol in internet:
  TCP and UDP
application
transport
network
data link
physical
انتقال انتها به انتهای منطقی
application
transport
network
data link
physical

## Slide 12: Transport protocols in the internet
TCP
  Connection-Oriented
  Reliable
  In-Sequence delivery
  Flow control
  Congestion control
UDP
  Connectionless
  Unreliable
  Non In-Sequence delivery
Services that are not provided:
  Implicit delay
  Implicit bandwidth
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
انتقال انتها به انتهای منطقی

## Slide 13: UDP: User Datagram Protocol
UDP segments might:
  Get lost
  Get delivered out of sequence
Connectionless:
  No handshaking is performed between sender and receiver
UDP applications:
  Multimedia streaming (lossy, rate sensitive)
  DNS
  SNMP (Simple Network Management Protocol)

## Slide 14: UDP segment structure
Doesn’t need connection (which helps reduce delay)
Easy (no need to keep the connection metadata in sender and receiver)
Small header (only 8 Byte)
Does not have congestion control
Source port
Destination port
32 بیت
Application data (message)
Length
Checksum
Segment length (header + data)
Why UDP exists?

## Slide 15: TCP: Overall Description
Full-Duplex service
  On one connection data can flow from both directions
  MSS: Maximum Segment Size
Connection-Oriented:
  Before data transformation sender and receiver perform a handshake
Flow control:
  Speed adjustment (sending rate of the sender is adjusted with the reading rate of the receiver)
Point to Point:
  One sender and one receiver
Reliable
Pipeline:
  TCP’s Flow control and congestion control set the window size

## Slide 16: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 17: Round-Trip Time and timer expiration
Question: How long should the expiration time be?
Should be longer than RTT
  But RTT is variable!
Too small: unnecessary re-send
Too long: TCP’s reaction to the lost segments will be slow.
Question: How to estimate RTT?
  SampleRTT: The time needed for a sample packet to turnaround
  Resent segments are not considered
Due to congestion in network, SampleRTT should be variable, so:
  Instead of one sample, multiple samples’ average is used

## Slide 18: Estimated Round Trip Time
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
Variable average with exponential weight
The weight of a specific SampleRTT is reduced exponentially with new samples.
Recommended value of  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)

## Slide 19: TCP: Re-sending scenarios
Early Expiration
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8
bytes of data
timeout
ACK=120
Seq=100, 20 bytes of data
ACK=120
SendBase=100
SendBase=120
SendBase=120
SendBase=92
Lost ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8 bytes of data
X
timeout
ACK=100

## Slide 20: TCP: Re-sending scenarios
X
Cumulative ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=120, 15 bytes of data
timeout
Seq=100, 20 bytes of data
ACK=120

## Slide 21: Quick re-transmission
Timer expiration can sometimes be too long:
  Long delay before retransmission of the lost packet
Detecting lost packets using the repetitive ACKs
  Mostly sender transmits a lot of packets continuously
  In case of packet loss, sender will receive lots of duplicate ACKs
If a Sender receives three duplicate ACKs for one packet it realizes that the next packet is lost
  So it won’t wait for the timeout and the re-transmission would happen
Qeuick re-transmission

## Slide 22: Quick re-transmission
X
Sender re-transmits after receiving three duplicate ACKs
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
timeout
ACK=100
ACK=100
ACK=100
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data

## Slide 23: TCP slow start
At first, sending rate is increased exponentially until the first loss happens:
  At start: cwnd = 1 MSS
  In each RTT, cwnd is being multiplied by two (for each ACK, cwnd is doubled)
Summary: Initial rate is slow but it grows exponentially.
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 24: TCP: Detection and reaction to packet wastage
Detected wastage by the timeout:
  cwnd=1 MSS
  Then cwnd’s value grows exponentially (like the slow start) until it reaches threshold, then grows on a linear basis
Detected wastage using 3 duplicate ACKs: TCP reno?
  Network is still able to deliver some of the packets
  Cwnd is divided by two then grows linearly
TCP taho? Always sets cwnd on 1 (either timeout happens or the 3 duplicate ACKs)

## Slide 25: TCP: From slow start to congestion prevention
Question: When should one migrate from exponential to linear growth
Answer: When cwnd is reached half it’s value

## Slide 26: Datagram networks
Handshake is not handled in network layer
Routers don’t store any state information about the end-to-end connections
Packets are forwarded using the destination address
1. Sending packet
application
transport
network
data link
physical
application
transport
network
data link
physical
2. Receiving packet

## Slide 27: Datagram forward table
1
2
3
Destination’s IP address is added to the packet
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
4 billion IP addresses, so instead of using one entry for each destination IP address, we use address range for each entry

## Slide 28: A router’s architecture
Two key functionality of a router:
Running algorithms/routing protocols (OSPF, BGP)
Forwarding the packets from the input link to the output link
High speed
Switching
Structure
Routing
Computer
Input ports
Output ports
Data forwarding level
(hardware)
Routing control and management level (software)
Forward table is calculated and is provided to the input ports

## Slide 29: Input port functionalities
Decentralized switching:
By checking the packet’s destination address and using the input port’s forwarding table, output port is searched
Purpose: processing the input port at the input link’s speed
Queuing: if the input packet rate is faster than the forwarding rate
Line ending
Datalink
Layer
Protocol
(Receive)
Search,
Forward
Queuing
Physical layer:
Bit receiving
Datalink layer:
Example,
Ethernet protocol
Switching
Structure

## Slide 30: Output ports
Buffering: when the input packet rate is faster than the transmission rate
Packet scheduling: Choosing the packets between the packets waiting in the queue to be transmitted
Line ending
Datalink
Layer
Protocol
(send)
Switching
Structure
Packet
buffer
Queuing

## Slide 31: Network layer in the internet
Forward
Table
Routing protocols
Choosing path
RIP, OSPF, BGP
IP protocol
Addressing standards
Datagram structure
Packet processing standards
ICMP protocol
Error report
Routing signaling
transport layer: TCP, UDP
link layer
physical layer
Network layer

## Slide 32: IP datagram structure
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
Header values:
20 Bytes TCP header
20 Bytes IP header
= 40 Bytes

## Slide 33: IP datagram segmentation
Network links have MTU (Maximum Transfer Unit)
The maximum data a datalink layer can carry
  Different link types have different MTUs
Big IP datagrams are divided into smaller datagrams
At the receiver these segments are attached together
Segmentation:
Input: A big datagram
Output: 3 small
datagrams
reassembly
…
…

## Slide 34: IPv4 addressing
IP address: a 32 bit ID for each host interface and router
Interface: The connection between host/router and physical link
An IP address for each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 35: IPv4 addressing
Question: How interfaces are connected together?
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Answer: Ethernet interfaces are connected together with Ethernet switches
Answer: Wireless interfaces are connected together with access points

## Slide 36: Subnetworks
IP address:
  Subnetwork part – most significant bits (leftmost part)
  Host part – least significant bits (rightmost part)
What is subnetwork?
  Interfaces that their subnet part has the same IP address
  They can connect together without a router
Network consisting 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 37: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  The subnet part of the addressing
  Addressing format: a.b.c.d/x where x represents the number of subnet bits
11001000 00010111 00010000 00000000
Subnet
Part
Host
Part
200.23.16.0/23

## Slide 38: ICMP (Internet Control Messaging Protocol)
Used to exchange information between network layer and routers
  Reporting the errors: network, host, port, protocol access
  Echo request/response
Resides in the network layer (above IP)
  ICMP messages are carried in IP packets
ICMP messages: type field, code field, first 8 Byte of the IP packet which caused the error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 39: Traceroute and ICMP
Source sends a sequence of UDP packets with improbable port number to the destination
  First sequence lifetime: TTL=1
  Second sequence lifetime: TTL=2
  …
  TTL: Time To Live
When the nth sequence of packets reach the nth router:
  Router drops the packets and sends ICMP message to source
  Message types of 11, code 0
  ICMP messages include router name and it’s IP address
Stopping criterion:
UDP segment reaches the destination host
ICMP message’s destination “Port not reachable” is sent back (type 3, code 3)
Source stops the packet transmission
3 probes
3 probes
3 probes

## Slide 40: IPv6: Motivation
Initial motivation: 32 bit addressing is going to be consumed very soon
Other motivations:
  Header’s format helps the speed of transmission and processing
  Header facilitates the quality of service
IPv6 datagram formats:
  Header with constant 40 Byte length
  No segmentation is allowed

## Slide 41: IPv6 datagram structure
Priority: detecting priority for a specific flow of packets
Flow label: detecting the flow that a packet belongs to
Next header: detecting the upper layer protocol (such as TCP or UDP)
Header length: 40 Byte
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 42: Other differences compared to IPv4
Header checksum: it is completely removed from network layer so that the processing time is reduced (transport layer protocols and datalink layer protocols do this job)
Options: Permitted but in the “next header” field
ICMPv6: new version of the ICMP
  Couple of additional messages, such as “too large packet”

## Slide 43
Routing protocols:
  Link state
  Distance vector
  Hierarchical routing
Routing in the internet
  RIP
  OSPF
  BGP
Routing Protocols

## Slide 44: Abstract graph
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Graph: G = (N,E)
N = Set of routers = { u, v, w, x, y, z }
E = Set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }

## Slide 45: Abstract graph: cost
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
C(x,y): cost of graph edge (x,y)
  Example: c(w,z) = 5
The cost of a normal link depends on the physical length, link speed, link congestion and financial cost of the link
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
Fundamental question: Which is the path with lowest const between
two node?
The natural goal of a routing algorithm is to find such paths.

## Slide 46: Routing algorithm categories
Global (centralized) or Distributed (decentralized)
Global:
All routers have complete information of the link topologies
Link state algorithms
Distributed:
Each router has only the info about it’s neighbors and their link costs
Each router performs a couple of repetitive computing and info exchange tasks with it’s neighbors
Distance vector algorithms
Static or dynamic
Static:
Paths change slowly during a long period of time
Dynamic:
Paths change along with the network traffic changes or changes in topology

## Slide 47: A link state routing algorithm
Dijkstra’s algorithm
Network topology and link costs are known for each node
  This is done by the “link state broadcast”
  All nodes have the same info
Calculates the optimal paths from a node (source) to all other nodes in the network
  Forward table is calculated for that node
After k iteration lowest cost paths are given for the other k destinations
Notations:
c(x,y): Link cost from x node to y; if these two are not neighbors this value is infinity
D(v): Current cost from the source to the destination v
P(v): previous node before v alongside the source to v
N’: A set of nodes that the optimal path to them is known

## Slide 48: Dijkstra’s algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'

## Slide 49: Dijkstra’s algorithm: example
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
Note:
Creating the tree containing optimal paths by visiting the previous nodes of a certain node
uwxvyz

## Slide 50: Dijkstra’s algorithm: example
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
v
x
y
w
z
(u,w)
(u,x)
(u,w)
(u,w)
(u,w)
destination
link
Optimal path and the u’s forward table

## Slide 51: Distance vector algorithm
Bellman-ford equation (dynamic programming)
Suppose
dx(y): the cost of the optimal path from x to y; hence:
v
The cost of link (x,y)
Minimum of all x’s neighbors
Cost from v node (x’s neighbor) to y
dx(y) = min {c(x,v) + dv(y) }

## Slide 52: An example of bellman-ford equation
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
It’s obvious that dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
According to bellman-ford equation:

## Slide 53: Distance vector algorithm
Dx(y): optimal cost estimation from x to y
Node x stores these routing informations:
  c(x,v): for each neighbor of v keeps it’s cost to there
  Dx = [Dx(y): y є N ]: x’s distance vector
  Distance vector of all it’s neighbors; for each v’s neighbor, x stores the vector: Dv = [Dv(y): y є N ]

## Slide 54: Distance vector algorithm
Main idea:
After a certain time interval, each node sends a copy of it’s distance vector to it’s neighbors
When x node receives a new distance vector from it’s neighbors, it updates it’s own distance vector using the bellman-ford equation.
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
After some iterations the estimated cost, Dx(y) will converge to the actual optimal cost dx(y) (‌Bert 1991)

## Slide 55: Distance vector algorithm
Interation: Each node will re-calculate it’s own distance vector in two cases:
Local link cost change (neighbor)
Receiving a new distance vector from one of it’s neighbors
Distributed:
This algorithm does not need network info to run. In fact, the only information needed to apply this algorithm is that each node will have access to the cost of the links that connect itself directly to it’s neighbors. The node will receive these info from it’s neighbors (distance vector changes)

## Slide 56
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
X’s table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
Y’s table
Z’s table
cost to
from

## Slide 57
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
X’s table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
Y’s table
Z’s table
cost to
from

## Slide 58: Hierarchical routing
Scalability: As the number of routers grow (maybe 600 million), computing, storage and info exchange’s overhead becomes a challenge
Execution independence:
Internet = network of networks
Each network admin may wish to control the way routing is done in their network
LS and DV algorithms’ viewpoint sees the routers as if they are similar and they try to solve the routing through one algorithm. But this viewpoint is weak by these two reasons:

## Slide 59: Hierarchical Routing
Organizing the routers in shape of Autonomous Systems (AS)
Each ISP contains one or more Autonomous Systems
The routers in an AS run the same routing protocol
  Intra-AS routing protocol
Routers inside different ASs can run different routing protocols
Gateway router: A router that has a link to a router from another AS

## Slide 60: Connected ASs
Forwarding table is configured by both the inter and intra-AS routing protocols
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
protocol
Inter-AS
Routing
protocol
Forward table
3c

## Slide 61: Intra-AS routing
Intra-AS protocols are also called interior gateway protocols - IGP
The most common intra-AS routing protocols:
  Routing Information Protocol - RIP
  Open Shortest Path First - OSPF

## Slide 62: RIP protocol
Is a distance vector protocol
  Cost criterion: hop count (at max 15), in other words, each link’s cost is 1
  Neighbor routers exchange their routing information each ~30 seconds (RIP advertising)
D
C
B
A
u
v
w
x
y
z
subnet hops
u 1
v 2
w 2
x 3
y 3
z 2
Hop counts from A to different subnets

## Slide 63: RIP: example
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
Routing table at the D router
w
x
y
z
A
C
D
B

## Slide 64: RIP: example
w
x
y
z
A
C
D
B
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
A
5
dest next hops
w - 1
x - 1
z C 4
…. … ...
A-to-D advertisement
Routing table at the D router

## Slide 65: RIP: damaged link, coverage
If a router will be unaware of one of it’s neighbor for more than 180 seconds it assumes that either the router or the link connecting to it is damaged
  Paths containing this neighbor will be invalid
  This failure will be reported to the neighbor routers
  Link failure state will propagate to the whole network quickly

## Slide 66: OSPF protocol
“open”: it’s open for public usage
Uses the link state algorithm
  Link state packets propagation
  Network topology at every node
  Path calculation using the Dijkstra’s algorithm
Each link’s cost is set by the network admin
A router that uses OSPF will propagate it’s routing information to all the routers in the same AS (and not only the neighbor routers).
IS-IS routing protocol: similar to OSPF

## Slide 67: Advance features of OSPF
Security: Message exchange of the OSPF routers are authenticated
Some same-costed paths: If some paths lead to the same destination with the same cost, OSPF permits all these paths to be used.
Support for single and multi-path:
  MOSPF uses the same topology database as OSPF
Hierarchical OSPF in big domains

## Slide 68: Hierarchical OSPF
Edge router
Backbone router
Area 1
Area 2
area 3
Backbone
Gateway
Router
Inner
routers

## Slide 69: Inter-AS routing in internet: BGP
Border Gateway Protocol (BGP): The de-facto internet standard for inter-AS routing
BGP lets the AS to:
  Access information is taken from neighbor AS: eBGP
  Access information to all routers in the AS: iBGP
  Determining good paths to other networks based on access information and policies
BGP lets subnets to announce themselves to the internet: “I am here”

## Slide 70: BGP basics
When AS3 advertises a prefix to AS1 (using 1c router):
  AS3 promises to forward the packets to that prefix
  AS3 can aggregate the prefixes in it’s advertisement (It can advertise multiple subnets)
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
Other nets
Other nets
BGP session: a set of TCP connections between two routers and the BGP messages that are transfers in between them
  Path advertisement based on the prefix network addresses
  Data transfer is done on semi-permanent TCP connections
BGP message

## Slide 71: BGP basics: path information distribution
Using eBGP session between 3a and 1c routers, AS3 sends the access information to AS1
  Then 1c router can use iBGP session to distribute the new prefix information to all routers in AS1
  1b router also uses eBGP session on the link 1b-2a to advertise the new access information to AS2
When router learns the new prefix, it creates an entry in it’s forward table
AS3
AS2
3b
3a
AS1
1c
1a
1d
1b
2a
2c
2b
eBGP session
iBGP session
Other nets
Other nets

## Slide 72: Datalink layer
Jargons:
Nodes: Hosts, routers, switches
Links: channels that connect two neighbor nodes
  Wired links
  Wireless links
Frame: Layer 2 packet
global ISP
Datalink layer is responsible for transferring the datagram from one node to it’s neighbor

## Slide 73: Analogy with the transportation systems
Travel from Sanandaj to Lausanne ( in Switzerland )
  Car: Sanandaj to Emam Khomaini airport in tehran
  Airplane: Tehran to Geneva
  Train: Geneva to Lausanne
Traveler == Datagram
Different transportation systems == Connection links
Transport state == Datalink layer protocol
Traveling agency == Routing algorithm

## Slide 74: Datalink layer services
Framing: Putting the datagram in a frame, adding the source and destination’s address and including the checksums for error detection and error correction
Link Access: Channel access protocol for when multiple nodes share a link
Reliable delivery: Implicit datagram delivery from a node to the other (this service is usually used for links with high error rate (such as wireless links))
  Question: Why both datalink layer and transport layer (TCP) provide a reliable service?

## Slide 75: Datalink layer services
Error detection:
  Errors caused by signal attenuation or electromagnetic noise
  Receiver detects the errors
  Sending back signal to the sender for re-transmission or dropping the frame
Error correction:
  Receiver detects error and corrects the corresponding bits
Half duplex and Full duplex links
  Half duplex links both ends can not send at the same time

## Slide 76: Where is the datalink layer implemented?
In each host most parts of the datalink layer is implemented in the NIC (Network Interface Card)
In a router, the datalink layer is implemented in it’s Line Cards
Datalink layer is implemented using a combination of both hardware and software
Controller
Physical
Transfer
cpu
Memory
Host Bus ( such as PCI)
NIC
application
transport
network
link
link
physical

## Slide 77: Inter-Adaptor communication
Sender:
  Putting the datagram in the frame
  Adding the checksum bits
Receiver:
  Error detection and correction calculations (if included)
  Datagram extraction and passing on to the upper layer
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame